## Slide 1: In Search of Low Cost Mobile Bandwidth to Provide Improved Connectivity to Underserved Areas
Niall Robinson, 22.08.2017

## Slide 2: The Problem Statement
Internet not available with acceptable bandwidth in less densely populated areas in Africa
Hinders user social media experiences
Mobile is the best medium to deliver high speed internet connectivity in rural areas
What’s needed?
  Low cost solutions including optimized backhaul
  Small footprint
  Standardized and scalable solution for all nodes

## Slide 3: Reference Model
BNG
UE
Control Platform
Radius Server
Internet
Access Router
NT
eNB
NB
BTS
Nx GbE
Service creation for all services incl. BRAS functions and LER IP edge functions.
Mobile Core CO
CO
Building
CP
Main CO
Core CO
Cab.
WDM- PON
EPC
PER
IP/MPLS/OTN Backbone
LER
PSTN
MSC
RNC
BSC
IPSec GW
UE
NT
eNB
NB
BTS
Nx GbE
UE
NT
eNB
NB
BTS
Nx GbE

## Slide 4: Reference Model
BNG
UE
Control Platform
Radius Server
Internet
Access Router
NT
eNB
NB
BTS
Nx GbE
Service creation for all services incl. BRAS functions and LER IP edge functions.
Mobile Core CO
CO
Building
CP
Main CO
Core CO
Cab.
WDM- PON
EPC
PER
IP/MPLS/OTN Backbone
LER
PSTN
MSC
RNC
BSC
IPSec GW
UE
NT
eNB
NB
BTS
Nx GbE
UE
NT
eNB
NB
BTS
Nx GbE

## Slide 5: LTE base station connectivity Technology selection
Both directions accommodated in one CWDM slot
BiDi CWDM
CWDM Filter
BiDi CWDM
CWDM Filter
One Fiber
Optimized for outdoor environment
  20nm CWDM grid is substantially wider than the 0.8nm DWDM grid
  Laser can drift freely for temperatures up to +85°C
  Passive filter technology
Negligible asymmetric delay – Meets LTE requirements by design
  By using CWDM BiDi both transmission directions have exactly the same fiber length
Technology: Coarse WDM Single Fiber Working
Single element filter

## Slide 6: 2 x 1GE SFW CWDM Bidi
16CSM/P-
East West
East West
East West
East West
East West
East West
East West
East West
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
Up to 2 x 1G per site
East/West protection
Single fibre strand

## Slide 7: 2 x 1GE SFW CWDM Bidi
16CSM/P-
East West
East West
East West
East West
East West
East West
East West
East West
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
Up to 2 x 1G per site
East/West protection
Single fibre strand

## Slide 8: 2 x 1GE SFW CWDM Bidi
16CSM/P-
East West
East West
East West
East West
East West
East West
East West
East West
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
Up to 2 x 1G per site
East/West protection
Single fibre strand

## Slide 9: 2 x 1GE SFW CWDM Bidi
16CSM/P-
East West
East West
East West
East West
East West
East West
East West
East West
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
Up to 2 x 1G per site
East/West protection
Single fibre strand

## Slide 10
16CSM/P-
16CSM/P-
XG120
16CSM/P-
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
CWDM Bidi directly plugged into aggregation device
Traffic terminated on FSP150 GE120 and aggregated into 1/2 x 10G interfaces
Hub Site Configuration
eNodeB Configuration
Passive solution
Active solution
Single interface BiDi CWDM SFP
East
West
Y cable filter
BiDi CWDM SFP plugged into FSP150
East
West
Y cable filter

## Slide 11: 2 x 10GE SFW CWDM Bidi Up to 8 access nodes on single fibre
16CSM/P-
East West
East West
East West
East West
East West
East West
East West
East West
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
Up to 2 x 10G per site
East/West protection
Single fibre strand

## Slide 12
16CSM/P-
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
CWDM Bidi directly plugged into aggregation device
Hub Site Configuration
eNodeB Configuration
Passive solution
Single interface BiDi CWDM SFP directly plugged into eNodeB
East
West
Y cable filter

## Slide 13: 2 x10GE Active solution
10GE Demarcation/ Transponders
16CSM/P-
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
CWDM Bidi directly plugged ADVA Transponders
Hub Site Configuration
Active 10GE solution
Media converter/1HU 5WCA transponders
16 x 10GE handoff to backbone
eNodeB Configuration
Single interface BiDi CWDM SFP
East
West
Y cable filter
2 x 10GE 850nm MM
Standard “grey” multimode handover to eNodeB
IP/MPLS/OTN Backbone

## Slide 14: Voyager – Packet Optical Solution
Voyager is an Open Optical Packet Transport box
The design for both hardware and software has been submitted to TIP, the Telecom Infra Project making this available to all
Voyager is a 1RU pizza box packet-optical solution.
  It has Layer 2 Forwarding Engine and Layer 3 Routing capabilities
ADVA supplies Voyager hardware and software – either:
  As a standalone entity for integration into disaggregated networks
  Integrated with ADVA Open Optical Layer and Management System
  Both options will be integrated into ADVA Commercial and Service offerings
Voyager

## Slide 15: 2 x10GE Active solution with Voyager
10GE Demarcation/ Transponders
16CSM/P-
16CSM/P-
λ 1 – λ8
λ 1 – λ8
8x
8x
CWDM Bidi directly plugged ADVA Transponders
Hub Site Configuration
Active 10GE solution
Media converter/1HU 5WCA transponders
4 x 10GE per QSFP port
eNodeB Configuration
Single interface BiDi CWDM SFP
East
West
Y cable filter
2 x 10GE 850nm MM
Standard “grey” multimode handover to eNodeB
4 x 200G Coherent DWDM connection to backbone
Voyager - Layer 2 Forwarding Engine and Layer 3 Routing capabilities

## Slide 16: Solution Comparison
10GE based solutions deliver lowest bandwidth cost and highest capacity
Active solution slightly more expensive than passive but has easier deployment and management attributes
Voyager can provide a cost effective multi-layer interface to IP/MPLS backbone
1GE
Passive
1GE
Active
10GE
Passive
10GE
Active
Cost per GE
Easy deployment
Active Management
Total bandwidth per eNodeB
2GE
20GE
Deployment restrictions
Limited Management

## Slide 17: Solution Expansion: Active monitoring of Fiber Plant
The integrity of the access fiber is monitored by measuring the reflection of a laser at 1650nm that is co-propagated with the traffic signal(s)
Normal Operation
Fiber-cut detection
Reflectance
Distance
Rayleigh scattering
Demarcation Reflector
The optical power of the reflection from the CPE/Far-end demarcation is monitored
The intensity of the reflected demarcation peak provides an estimate of the insertion loss of the link
A fiber cut or increased insertion loss is detected as this reduces the demarcation reflection peak
By measuring the Rayleigh scattering power the location of the fiber-cut can be detected
Reflectance
Distance
Rayleigh scattering
Fiber-cut

## Slide 18: Summary
Very lost cost, low resource consumption backhaul network architectures are possible using a combination of:
  Pluggable optics
  Single fiber working (BiDi) architectures
  Open source packet optical platform Voyager
Solution extensions include:
  Protection capabilities for redundant path operation. Increases cost but also increases network resiliency
  Dual fiber working (if fibers are more readily available)
  Low cost fiber monitoring capabilities to continuously monitor fiber quality / link availability
Further cost optimizations are under study

## Slide 19: Thank You
IMPORTANT NOTICE
The content of this presentation is strictly confidential. ADVA Optical Networking is the exclusive owner or licensee of the content, material, and information in this presentation. Any reproduction, publication or reprint, in whole or in part, is strictly prohibited.
The information in this presentation may not be accurate, complete or up to date, and is provided without warranties or representations of any kind, either express or implied. ADVA Optical Networking shall not be responsible for and disclaims any liability for any loss or damages, including without limitation, direct, indirect, incidental, consequential and special damages, alleged to have been caused by or in connection with using and/or relying on the information contained in this presentation.
Copyright © for the entire content of this presentation: ADVA Optical Networking.
Niall Robinson
Vice President
Global Business Development
Phone: +1 972 759 1262
Fax: +1 972 759 1201
Mobile: +1 978 933 1081
nrobinson@advaoptical.com
ADVA Optical Networking NA. Inc.
2301 N. Greenville Avenue
Suite 300
Richardson, TX 75082
USA
www.advaoptical.com

## Slide 20: Backup Slides

## Slide 21: Passive vs Active
Pluggables, directly connected to radio equipment
East West
Line
East
Line
West
Filter in cable assembly
Direct Optics Radio Vendor
Radio equipment independent of CWDM interfaces
Line
East
Line
West
Filter in cable assembly
Demarcation/transponer Based
1GE/10GE demarcation / 10GE Transponders
East West
10G XFP
BiDi CWDM
1G SFP
BiDi CWDM
1CSM+#Cxxxx

## Slide 22: Key Features and Benefits
Service agnostic OTDR technology for 24x7 in-service fiber link monitoring
Cost-optimized solution for real-time service assurance
Automated fiber fault detection, localization and notification
Ease of use featuring intuitive GUI, integrated with various GISs, open SNMP-based NBI, integrated into the ADVA Network Management System
Proven technology, deployed with major fixed and mobile network operators
Unique in-service fiber monitoring: cost-efficient, fast and reliable